## Slide 1
IoT-Based Gas & Fire Safety Alert System
Simulated in Wokwi using ESP32 and MQTT
Bariya Sahil | 2305101270029 | BCA(H) | Div C
Atmiya Patel | 2305101270218 | BCA(H) | Div C

## Slide 2
Problem & Objective
Problem
Gas leaks and small fires often go unnoticed until damage is done
Manual monitoring is unreliable, especially at night or when nobody is home
Delayed alerts increase risk to life and property
Objective
Detect gas leakage and abnormal heat automatically in real time
Trigger local alarm (buzzer + LED) instantly
Send remote alerts over the internet using MQTT

## Slide 3
Components Used (Wokwi)
Component | Role
ESP32 DevKit | Microcontroller with built-in WiFi
Gas Sensor (MQ-2 style) | Measures gas concentration (analog)
DHT22 Sensor | Measures temperature to detect fire / heat
Buzzer | Audible alarm
Red / Green LED | Alert / safe status indicator
Resistors (220 ohm) | Current limiting for LEDs
MQTT broker (HiveMQ) | Cloud message delivery for remote alerts

## Slide 4
Circuit Connections
Part | Pin | ESP32 GPIO
Gas sensor | AOUT | GPIO 34
DHT22 | SDA | GPIO 15
Buzzer (+) | Positive | GPIO 25
Red LED (via resistor) | Anode | GPIO 26
Green LED (via resistor) | Anode | GPIO 33
All sensors | VCC / GND | 3V3 / GND

## Slide 5
Working Principle
1. Sense
Gas level and temperature are read every 2 seconds
2. Decide
Alarm if gas > 2000 or temperature > 50 C
3. Alert
Red LED and buzzer ON; green LED shows safe state
4. Publish
JSON status sent to MQTT topic for remote monitoring

## Slide 6
Core Logic (Arduino C++)
int gas = analogRead(GAS_PIN);
float temp = dht.readTemperature();
bool alarm = (gas > GAS_THRESHOLD) ||
(temp > TEMP_THRESHOLD);
digitalWrite(RED_LED, alarm);
digitalWrite(GREEN_LED, !alarm);
digitalWrite(BUZZER_PIN, alarm);
client.publish(TOPIC, msg.c_str());
Full code provided in sketch.ino

## Slide 7
Results & Future Scope
Results
Alarm triggers when gas slider crosses threshold
Alarm triggers when temperature crosses 50 C
Status messages received live on the MQTT client
Green LED confirms normal, safe condition
Future Scope
Add a real flame sensor and smoke sensor on hardware
SMS / WhatsApp alerts via cloud services
Automatic exhaust fan or valve shut-off using a relay
Mobile dashboard with history and analytics